## Slide 1: MapServer and OGC Web Services
http://ms-ogc-workshop.maptools.org/

## Slide 2: Outline
Web Services / Interoperability
Applying OGC Web Services with MapServer:
  OGC:WMS
    with OGC:SLD
  OGC:WFS/OGC:GML
  OGC:WCS
  OGC:SOS
  OGC:WMC
  OGC:Filter
  Brokering to distributed Web Services for Geocoding
Future goodies / Nice-to-Haves / Issues

## Slide 3: Workshop
Homepage
  http://ms-ogc-workshop.maptools.org/
Download
  http://ms-ogc-workshop.maptools.org/dl/
CVS
  CVSROOT
    :pserver:cvsanon@cvs.maptools.org:/cvs/maptools/cvsroot
  Module: ms_ogc_workshop
Support
  mapserver-users mailing list

## Slide 4: Workshop Package
Install
  Extract ms_ogc_workshop.zip (WinZip)‏
    Extract to root of drive letter of ms4w location (i.e. C:\)‏
    Make sure “Use Folder Names” is checked
    Extracts into existing ms4w directory structure
Base Directory:
  \ms4w\apps\ms_ogc_workshop\
Startup:
  Start Apache:
    \ms4w\Apache\bin\Apache.exe
  Go to: http://127.0.0.1/ms_ogc_workshop/index.html

## Slide 5: Web Services / Interoperability
Distributed data through services interface
  Less redundant data
  Authoritative
  More effective data management
  Connect rather than hoard
Transparent / cooperative

## Slide 6: Web Services / Interoperability
Based on open specifications
  W3C, OGC
Normalizes playing field, independent of:
  Operating System
  Programming Languages
  Development Environments
How?
  Web Services!

## Slide 7: Geospatial Interoperability
“Geospatial Interoperability is the ability for two different software systems to interact with geospatial information. Interoperability between heterogeneous computer systems is essential to providing geospatial data, maps, cartographic and decision support services, and analytical functions. Geospatial interoperability is dependent on voluntary, consensus-based standards... These geospatial standards are essential to advancing data access and collaborations in e-Government, natural hazards, weather and climate, exploration, and global earth observation.”
  Geospatial Interoperability (GI) Return on Investment Study Report , NASA, April 2005
    http://gio.gsfc.nasa.gov/docs/ROI%20Study.pdf

## Slide 8: Web Services Defined
Web Service = any software which makes itself available over the Internet and uses a standard XML messaging system
XML makes this happen
Provides more control to application developer (raw vs. refined goods)‏

## Slide 9: Web Services Architecture Approach
Applications
e.g., Community Water Quality,
Climate Change Monitoring,
Site Assessment
Services
e.g., Water Quality Index Service
Gazetteer service,
Web Map Service
Data
e.g., water quality, quantity,
topographic,
thematic, imagery,
toponymy, metadata
Users
Other
Applications
For Example…
A community website which calculates water quality for a given community
uses
Gazetteer service,
Water Quality Index Service
Web Map Service
based on
Geographical Names,
Road network features
Base maps

## Slide 10: Open Geospatial Consortium (OGC)‏
Circa 1994
Web Services for Geospatial Interoperability
“Develop first, then spec” approach

## Slide 11: OGC Specifications
WMS
WFS
WCS
WMC
GML
SLD
SOS, OM
Filter
Catalog
WCTS
GO-1
OWS Common
Grid Coverages
Location Services
Simple Features
  CORBA
  SQL
  OLE/COM
Bold = Supported by MapServer

## Slide 12: MapServer and OWS
Enabling OWS in MapServer
  Build software with:
  --with-wms \
  -–with-wmsclient \
  –-with-wfs \
  –-with-wfsclient \
  -–with-wcs
  --with-sos
  NB: dependent libraries needed
    Read documentation
    Get predefined Builds
      Windows, MS4W, FGS

## Slide 13: MapServer and OWS
Enabling OWS in MapServer
  Same old MapServer; just populate mapfiles with appropriate directives
  MapServer OGC documentation HOWTOs

## Slide 14: MapServer and OWS
Unified OWS Metadata!!
  MapServer now supports “ows_*” type metadata declarations
  OWSs with common metadata element names can use this
  Cuts down on mapfile size
  Less management of metadata

## Slide 15: MapServer and OWS
Instead of:
  “wms_title” “Land Use”
  “wfs_title” “Land Use”
How about:
  “ows_title” “Land Use”
  Satisfies anything “[wms|wfs|wcs|gml|sos]_title”
You can still set service-specific metadata if you need to, which overrides “ows_*”

## Slide 16: OGC WMS
Provides images of map data defined by a geographic / spatial component
Provides point based query functionality
Interoperable means of map compositing from n servers
‘just-in-time’ approach

## Slide 17
Web Browser
Viewer Client
Map Server
Map Server
Map Server
Map Server
internet
Web Map Servers
http://ceoware2.ccrs.nrcan.gc.ca/cubewerx/cubeserv/cubeserv.cgi?version=1.1.0&service=wms&request=GetMap&bbox=-72.478366,40.108703,-55.746366,50.135369&width=500&height=300&srs=EPSG:4326&layers=L7O_B743:CEOWARE2&format=image/gif&transparent=TRUE&exceptions=application/vnd.ogc.se_inimage&styles=default
http://wms.cits.rncan.gc.ca/cgi-bin/cubeservcubeserv.cgi?version=1.1.0&service=wms&request=GetMap&bbox=-72.478366,40.108703,-55.746366,50.135369&width=500&height=300&srs=EPSG:4326&layers=ROUTE_1:BNDT/NTDB-250K&format=image/gif&transparent=TRUE&exceptions=application/vnd.ogc.se_inimage&styles=default
http://ceoware2.ccrs.nrcan.gc.ca/cubewerx/cubeserv/cubeserv.cgi?
version=1.1.0&service=wms&request=GetMap&srs=EPSG:4326&
bbox=-80.279475,43.082972,79.281178,43.682405&width=500&height=300
&layers=L7O_B743:CEOWARE2&format=image/gif&transparent=TRUE
&exceptions=application/vnd.ogc.se_inimage&styles=default
http://wms.cits.rncan.gc.ca/cgi-bin/cubeserv.cgi?
version=1.1.0&service=wms&request=GetMap&srs=EPSG:4326&
bbox=-80.279475,43.082972,79.281178,43.682405&width=500&height=300
&layers=ROUTE_1:BNDT/NTDB-250K&format=image/gif&transparent=TRUE
&exceptions=application/vnd.ogc.se_inimage&styles=default

## Slide 18: OGC WMS
HTTP based (GET or POST)‏
Currently version 1.1.1
Operations
  GetCapabilities
  DescribeLayer
  GetMap
  GetFeatureInfo
    Operation keywords are CaSe-InSeNsItIvE
    Opearation values are case-sensitive

## Slide 19: OGC WMS
GetCapabilities
  Provides XML of service functionality metadata, and layer metadata
  Parameters
    Version (version of specification)‏
    Service (multiple services may exist from this service, e.g. WMS, WFS, WCS)‏
    Request (GetCapabilities)‏
E.g.
http://127.0.0.1/cgi-bin/mapserv.exe?map=/ms4w/apps/ms_ogc_workshop/service/config.map&version=1.1.1&service=WMS&request=GetCapabilities

## Slide 20: OGC WMS
Formats
  transparency
Exceptions
Choose accordingly
Layers
  Data offerings
  Nesting / Grouping

## Slide 21: OGC:WMS
DescribeLayer
  OPTIONAL operation to provide more information about a WMS layer (WFS, etc.)‏
  Parameters
    VERSION
    SERVICE
    REQUEST
    LAYERS
  http://127.0.0.1/cgi-bin/mapserv.exe?map=/ms4w/apps/ms_ogc_workshop/service/config.map&version=1.1.1&service=WMS&request=DescribeLayer&layers=rivers

## Slide 22: Web Map Service (WMS)‏
GetMap
  Returns graphic image of data based on area of interest, data, etc.
  Image, not features, not attributes
Notes: WMS
- serve image maps
- GetCapabilities, GetMap, GetFeatureInfo
- GetFeatureInfo will deprecate to WFS

## Slide 23: Web Map Service (WMS)‏
Parameters
  version (version of specification)‏
  service (multiple services may exists from this service, e.g. WMS, WFS, WCS)‏
  request (GetMap)‏
  format (image format to be returned)‏
    Get this from GetCapabilities info
Notes: WMS
- serve image maps
- GetCapabilities, GetMap, GetFeatureInfo
- GetFeatureInfo will deprecate to WFS

## Slide 24: Web Map Service (WMS)‏
Parameters
  bbox (spatial area of interest, i.e. minx,miny,maxx,maxy)‏
  srs (reference system / projection of bounding box coordinates
    EPSG (http://www.epsg.org/)‏
    Get supported SRSs from GetCapabilities
  Most widely used SRS is EPSG:4326
    Lat/long geographic (WGS84)‏
Notes: WMS
- serve image maps
- GetCapabilities, GetMap, GetFeatureInfo
- GetFeatureInfo will deprecate to WFS

## Slide 25: Web Map Service (WMS)‏
Parameters
  width (output image width)‏
  height (output image height)‏
  layers (data desired to be visualized)‏
    Get this from GetCapabilities info
    Comma-separated list
      Eg. Layers=elevation,roads,railways,…
      First list item is bottom most output layer
Notes: WMS
- serve image maps
- GetCapabilities, GetMap, GetFeatureInfo
- GetFeatureInfo will deprecate to WFS

## Slide 26: Web Map Service (WMS)‏
Parameters
  TIME
    ISO 8601 formatted timestring
    Single point
    Frequency
    Range
    Current
  Not all WMS implementations support TIME
Notes: WMS
- serve image maps
- GetCapabilities, GetMap, GetFeatureInfo
- GetFeatureInfo will deprecate to WFS

## Slide 27: Web Map Service (WMS)‏
Parameters
  Styles (desired portrayal of data)‏
    Get this from GetCapabilities info per layer
    Comma-separated list
      e.g.. layers=elevation,roads,railways&styles=default,red,blue
      Style list MUST align with layer list
      Empty list value for non styled layers
      e.g. to style ONLY railways layer: layers=elevation,roads,railways&styles=,,blue
Notes: WMS
- serve image maps
- GetCapabilities, GetMap, GetFeatureInfo
- GetFeatureInfo will deprecate to WFS

## Slide 28: Web Map Service (WMS)‏
Parameters
  Styles and SLD
    SLD enables remote classification and symbolization of data
    Overrides server-based styles if request from user
    To use in GetMap, SLD document must exist over HTTP, and cited in GetMap request
      &sld=http://localhost/ms_ogc_workshop/sld/rivers.sld
      OR &sld_body=<entire_sld_document>
      (consider HTTP POST for SLD_BODY)‏
    More info on SLD later
Notes: WMS
- serve image maps
- GetCapabilities, GetMap, GetFeatureInfo
- GetFeatureInfo will deprecate to WFS

## Slide 29: Web Map Service (WMS)‏
Parameters
  transparent (whether to make non-opaque data pixels transparent
    Either TRUE or FALSE
    Useful for layering data from multiple remote WMS services atop eachother for map composition
    Depends on image format (JPEG is not transparent)‏
    Depends on web browser support
      GIF transparency is supported in all browsers
      PNG transparency support in newer browsers
  bgcolor (optional background color of image)‏
Notes: WMS
- serve image maps
- GetCapabilities, GetMap, GetFeatureInfo
- GetFeatureInfo will deprecate to WFS

## Slide 30: Web Map Service (WMS)‏
Parameters
  Exceptions (how to handle errors)‏
  Can be caused by:
    Server malfunction
    Invalid client syntax (missing required values, etc.)‏
  application/vnd.ogc.se_xml
  application/vnd.ogc.se_inimage
  application/vnd.ogc.se_blank
Notes: WMS
- serve image maps
- GetCapabilities, GetMap, GetFeatureInfo
- GetFeatureInfo will deprecate to WFS

## Slide 31: Web Map Service (WMS)‏
Parameters
  Exceptions
    Which one should I use?
    application/vnd.ogc.se_inimage
      Useful for easily visualizing errors in your app
      Can also be ugly to the end-user / audience
    application/vnd.ogc.se_blank
      Returns a blank image
      Difficult to recognize what type or error has occurred
    application/vnd.ogc.se_xml
      Returns an XML exception document
      Difficult to decode if your app is requesting an image type
  Choose accordingly
Notes: WMS
- serve image maps
- GetCapabilities, GetMap, GetFeatureInfo
- GetFeatureInfo will deprecate to WFS

## Slide 32: Web Map Service (WMS)‏
E.g.:
http://127.0.0.1/cgi-bin/mapserv.exe?map=/ms4w/apps/ms_ogc_workshop/service/config.map&version=1.1.1&service=WMS&request=GetMap&srs=EPSG:4326&bbox=-180,-90,180,90&format=image/png&layers=land_shallow_topo_2048,rivers&styles=,&transparent=true&width=500&height=300
Notes: WMS
- serve image maps
- GetCapabilities, GetMap, GetFeatureInfo
- GetFeatureInfo will deprecate to WFS

## Slide 33: Web Map Service (WMS)‏
GetFeatureInfo
  Performs point-based queries on map data
  No ability for complex, expression-like queries
    This is covered the WFS specification
Notes: WMS
- serve image maps
- GetCapabilities, GetMap, GetFeatureInfo
- GetFeatureInfo will deprecate to WFS

## Slide 34: Web Map Service (WMS)‏
GetFeatureInfo
  Parameters
  <all GetMap parameters>
    request=GetFeatureInfo instead of GetMap
    Pass on ALL GetMap keyword-value pairs as if performing a GetMap request
    x (pixel value in X image coordinates)‏
    y (pixel value in Y image coordinates)‏
    query_layers (layers to be queried)‏
      Can be one or multiple layers
      This does not substitute passing the layers parameter
Notes: WMS
- serve image maps
- GetCapabilities, GetMap, GetFeatureInfo
- GetFeatureInfo will deprecate to WFS

## Slide 35: Web Map Service (WMS)‏
Parameters
  info_format
    Get this from GetCapabilities info
    Common formats
      HTML
        difficult to parse
      GML.1
        XML-based
        Lacks common definition structure between vendor implementations
    See http://127.0.0.1/ms_ogc_workshop/ for examples
Notes: WMS
- serve image maps
- GetCapabilities, GetMap, GetFeatureInfo
- GetFeatureInfo will deprecate to WFS

## Slide 36: OGC:WMS
Enabling in MapServer
  MapServer must be built with --with-wms
  Through metadata elements in mapfile
    “ows_*” or “wms_*” type metadata
      These drive interface content
    see wms-server howto

## Slide 37: OGC:WMS
The Server URL thing
MapServer needs CGI “map” keyword (i.e. MS_MAPFILE environment variable) to drive interface
This can be tacked on to server URL as the base WMS server URL prefix
If you want, you can hide mapfile via HTTPD settings
See:
  http://127.0.0.1/ms_ogc_workshop/service/hide-mapfile-location.php

## Slide 38: Publishing OGC:WMS
    Go to dir: /ms4w/apps/ms_ogc_workshop/service/
    Open exercise.map
    Add all WMS contact information in mapfile WEB METADATA
    Try new server URL:
      http://127.0.0.1/cgi-bin/mapserv.exe?map=/ms4w/apps/ms_ogc_workshop/service/exercise.map
      Perform a GetCapabilities request
Notes: WMS
- serve image maps
- GetCapabilities, GetMap, GetFeatureInfo
- GetFeatureInfo will deprecate to WFS

## Slide 39: Publishing OGC:WMS
    Add the rivers layer to the mapfile to publish as a WMS layer
    See wms-server howto
    Color should 0 0 255
    Data is in
      /ms4w/apps/ms_ogc_workshop/data/rivers
Notes: WMS
- serve image maps
- GetCapabilities, GetMap, GetFeatureInfo
- GetFeatureInfo will deprecate to WFS

## Slide 40: Publishing OGC:WMS
  Save to disk?
    Capabilities responses for WMS use a MIME type which web browsers are not familiar with:
      application/vnd.ogc.wms_xml
    You can configure your web browser to launch a specific application when it encounters this MIME type
      i.e. Firefox: add to mimeTypes.rdf:
        <RDF:Description RDF:about="urn:mimetype:handler:application/vnd.ogc.wms_xml"
        NC:alwaysAsk="true"
        NC:saveToDisk="true">
        <NC:externalApplication RDF:resource="urn:mimetype:externalApplication:text/xml"/>
        </RDF:Description>
Notes: WMS
- serve image maps
- GetCapabilities, GetMap, GetFeatureInfo
- GetFeatureInfo will deprecate to WFS

## Slide 41: OGC:SLD
“Add-on” specification to OGC:WMS
  “SLD-enabled WMS”
Enables custom styling
  Data at the server does not have to change
  Client sends SLD XML document for symbolization, etc.
    Either as URL or within BODY of the request
      If URL, it MUST be resolvable and accessible by the WMS server

## Slide 42: OGC:SLD
Additional OGC:WMS operations with OGC:SLD:
  GetLegendGraphic
  GetStyles
  PutStyles

## Slide 43: OGC:SLD
GetLegendGraphic
Dynamic legend icon for a given layer
Parameters
  VERSION
  SERVICE
  REQUEST
  FORMAT
  LAYER
  SLD

## Slide 44: OGC:SLD
GetStyles
Returns OGC:SLD for a given layer
Parameters
  VERSION
  SERVICE
  REQUEST
  LAYERS

## Slide 45: OGC:SLD
PutStyles
Stores SLD document on WMS server
Not supported by MapServer

## Slide 46: OGC:SLD
Enabling in MapServer
Not much, really
  MapServer code (CGI) basically exposes and converts CLASS objects to SLD constructs
  Also via PHP MapScript to mapObj or layerObj
  See here for SLD examples:
    http://127.0.0.1/ms_ogc_workshop/index.html

## Slide 47: Consuming OGC:WMS
    MapServer, on your behalf, can connect to OGC:WMS as well
    Takes care of client code specifics (whew!)‏
    Specific LAYER METADATA elements in mapfile
    See wms-client-howto
    http://127.0.0.1/ms_ogc_workshop/client/wms/demo_init.html
    http://127.0.0.1/ms_ogc_workshop/client/wms/demo.map
Notes: WMS
- serve image maps
- GetCapabilities, GetMap, GetFeatureInfo
- GetFeatureInfo will deprecate to WFS

## Slide 48: Consuming OGC:WMS
    Go to dir:
      /ms4w/apps/ms_ogc_workshop/client/wms/satellite/
    Add a WMS layer to demo.map
      World Soil Resources
      Server:
        http://geonetwork3.fao.org/cgi-bin/wms?map=/GeoNetwork_data/01100-01199/1111/wms/1111.map
      Layer name:
        world_soil_resources
      Hints:
      Do a GetCapabilities to get more info on the layer, formats, projections, version, etc.
      See wms-client-howto
      More examples of remote global layers in:
        http://127.0.0.1/ms_ogc_workshop/client/wms/satellite/servers.txt
Notes: WMS
- serve image maps
- GetCapabilities, GetMap, GetFeatureInfo
- GetFeatureInfo will deprecate to WFS

## Slide 49: Consuming OGC:WMS and SLD
    Go to dir:
      /ms4w/apps/ms_ogc_workshop/client/wms/satellite/
    Add another WMS layer to demo.map
      Bird Studies Canada Important Bird Locations
      Server:
        http://www.bsc-eoc.org/cgi-bin/bsc_ows.asp
      Layer name:
        IBA
    Add the following SLD document:
        http://devgeo.cciw.ca/ms_tmp/iba_sld.xml
    Hints:
      Look at the SLD document to get a feel of what’s going on
      See sld-howto and workshop SLD examples
      If you’re ambitous, set “wms_sld_body” to “AUTO”, and generate a CLASS object, which generates the SLD on the fly in the WMS GetMap request
Notes: WMS
- serve image maps
- GetCapabilities, GetMap, GetFeatureInfo
- GetFeatureInfo will deprecate to WFS

## Slide 50: OGC:WFS
Feature level access to spatial data (vectors)‏
Rich query interface
Returns GML
Transactional capability
Security considerations for OGC:WFS-T
  MapServer supports basic WFS
    No transactions
Notes: WFS
- feature level access to geographic data
- GML type return of data
- transactional capability (INSERT,UPDATE,DELETE)‏
- security issues (accidental/implied data corruption)‏

## Slide 51: OGC:WFS
Operations
  GetCapabilities
  DescribeFeatureType
  GetFeature

## Slide 52: OGC:WFS
GetCapabilities
Same idea as OGC:WMS GetCapabilities
Parameters
  VERSION
  SERVICE
  REQUEST
http://127.0.0.1/cgi-bin/mapserv.exe?map=/ms4w/apps/ms_ogc_workshop/service/config.map&version=1.0.0&service=WFS&request=GetCapabilities

## Slide 53: OGC:WFS
DescribeFeatureType
Provides an outline of the structure of a feature type (fields, etc.)‏
Analogous to SQL describe <table> command
Parameters
    VERSION
    SERVICE
    REQUEST
    TYPENAME
http://127.0.0.1/cgi-bin/mapserv.exe?map=/ms4w/apps/ms_ogc_workshop/service/config.map&version=1.0.0&service=WFS&request=DescribeFeatureType&typename=rivers

## Slide 54: OGC:WFS
GetFeature
Gimme data!
Parameters
  VERSION
  SERVICE
  REQUEST
  TYPENAME
  FILTER (optional)‏
  BBOX (can also be done through FILTER)‏
  E.g.: see index.html

## Slide 55: OGC:WFS
Enabling in MapServer
  MapServer must be built with --with-wfs
  Through metadata elements in mapfile
    “ows_*” or “wfs_*” type metadata
      These drive interface content
    see wfs-server howto
    Layers must contain “DUMP TRUE”

## Slide 56: Consuming OGC:WFS
    MapServer, on your behalf, can connect to OGC:WFS as well
    Takes care of client code specifics (whew!)‏
    Specific LAYER METADATA elements in mapfile
    See wfs-client-howto
    http://127.0.0.1/ms_ogc_workshop/client/wfs/demo_init.html
    http://127.0.0.1/ms_ogc_workshop/client/wfs/demo.map
Notes: WMS
- serve image maps
- GetCapabilities, GetMap, GetFeatureInfo
- GetFeatureInfo will deprecate to WFS

## Slide 57: OGC:GML
    Text-based, portable data format
    Self-describing, XML
    GML schemas define geospatial objects for you
    YOU define what’s specific to your data
      attributes, etc.
Notes: WMS
- serve image maps
- GetCapabilities, GetMap, GetFeatureInfo
- GetFeatureInfo will deprecate to WFS

## Slide 58: OGC:GML
    Any GML parser can read your data!!
    Smarter components which are based on the GML standard
Notes: WMS
- serve image maps
- GetCapabilities, GetMap, GetFeatureInfo
- GetFeatureInfo will deprecate to WFS

## Slide 59: Serving OGC:GML
    GML usually comes from a OGC:WFS
    MapServer can also serve up static files
      OGR supports GML2
      Certain structure required for OGR to recognize content model
      Dataset/record type hierarchy
    You can serve up GML:
      From GML documents you made yourself
      From GML documents you copied from elsewhere
      By doing nothing; OGC:WFS offers GML already
Notes: WMS
- serve image maps
- GetCapabilities, GetMap, GetFeatureInfo
- GetFeatureInfo will deprecate to WFS

## Slide 60: Serving OGC:GML
    Making it happen
      CONNECTIONTYPE OGR
      CONNECTION “/path/to/gml/document”
      The rest is like any other LAYER object definition in the mapfile
    OGR processing
      Creates and caches *.gfs overview type file when first reading the data
      Quicker for subsequent data scans
Notes: WMS
- serve image maps
- GetCapabilities, GetMap, GetFeatureInfo
- GetFeatureInfo will deprecate to WFS

## Slide 61: Serving OGC:GML
    MapServer now supports GML3!
      via WFS supports both GML2 and GML3
      Same as serving GML2 for WFS
      WFS requests should have:
        DescribeFeatureType “outputFormat=XMLSCHEMA”
        DescribeFeatureType “outputFormat=SFE_XMLSCHEMA”
        GetFeature “outputFormat=GML3”
        GetFeature “outputFormat=GML2”
Notes: WMS
- serve image maps
- GetCapabilities, GetMap, GetFeatureInfo
- GetFeatureInfo will deprecate to WFS

## Slide 62: Serving OGC:GML
  Check out mums.gml for an example
  Check out mums.xsd for the XML Schema definition
    MapServer doesn’t necessarily use the .xsd
    Good practice nonetheless for validating XML parsers
Notes: WMS
- serve image maps
- GetCapabilities, GetMap, GetFeatureInfo
- GetFeatureInfo will deprecate to WFS

## Slide 63: Serving OGC:GML
  Try creating your own document by copying/pasting the mums examples
  Update reference to your new data in demo.map
  Now you’re a GML guru 
Notes: WMS
- serve image maps
- GetCapabilities, GetMap, GetFeatureInfo
- GetFeatureInfo will deprecate to WFS

## Slide 64: OGC:Filter
“Add on” specification to OGC:WFS
Custom XML query language
SQL in XML, almost
Spatial and aspatial query capabilities
  Logical
  Spatial
  Comparative

## Slide 65: OGC:Filter
SQL:
  select * from roads where roadtype = 1
OGC:Filter:
<Filter>
  <PropertyIsEqualTo>
    <PropertyName>roadtype</PropertyName>
    <Literal>1</Literal>
  </PropertyIsEqualTo>
</Filter>

## Slide 66: OGC:Filter
Enabling in MapServer
Not much, really
  Handled by MapServer OGC:WFS code
  E.g.:
    http://127.0.0.1/ms_ogc_workshop/filter/index.html
  See MapServer Filter howto

## Slide 67: Exercise
Add WFS client layer and client side filter encoding to /ms4w/apps/ms_ogc_workshop/client/wfs-filter/demo.map
Use OWS server:
    http://www2.dmsolutions.ca/cgi-bin/mswfs_filter
  Add as remote WFS layer
  Create the following filters:
    WHERE NAME = ‘Digby’
    WHERE NAME LIKE ‘Syd%’
    WHERE NAME = ‘Digby’ or NAME LIKE ‘Syd%’
Application http://127.0.0.1/ms_ogc_workshop/client/wfs-filter/demo_init.html
Helpers
  http://www2.dmsolutions.ca/cgi-bin/mswfs_filter?SERVICE=WFS&version=1.0.0&Request=GetCapabilities
  http://www2.dmsolutions.ca/cgi-bin/mswfs_filter?SERVICE=WFS&version=1.0.0&Request=DescribeFeatureType&TYPENAME=popplace
  See Filter examples for help
  See MapServer Filter howto and MapServer WFS client howto

## Slide 68
result map map file /ms4w/apps/ms_ogc_workshop/client/wfs-filter/demo_answer.map
result application : http://127.0.0.1/ms_ogc_workshop/client/wfs-filter/demo_init_answer.html
LAYER
NAME popplace
GROUP "VECTOR"
TYPE POINT
STATUS ON
CONNECTIONTYPE WFS
CONNECTION "http://www2.dmsolutions.ca/cgi-bin/mswfs_filter?"
PROJECTION
"init=epsg:42304"
END
METADATA
"wfs_connectiontimeout" "60"
"wfs_version" "1.0.0"
"wfs_service" "WFS"
"wfs_typename" "popplace"
"wfs_latlonboundingbox" "-65.4238 43.3796 -60.2557 47.7669"
# WHERE NAME = 'Digby'
#"wfs_filter" "<PropertyIsEqualTo><PropertyName>NAME</PropertyName><Literal>Digby</Literal></PropertyIsEqualTo>"

## Slide 69
LABELITEM "NAME"
CLASS
NAME "popplace"
STYLE
COLOR 255 0 0
SYMBOL 'circle'
SIZE 6
END
LABEL
COLOR 255 0 0
FONT fritqat-italic
TYPE truetype
SIZE 8
POSITION AUTO
PARTIALS FALSE
END
END #class
END#layer

## Slide 70: OGC:WCS
The raster equivalent to OGC:WFS
Provides “real” raster data
  DEM
  GeoTIFF

## Slide 71: OGC:WCS
Operations
  GetCapabilities
  DescribeCoverage
  GetCoverage

## Slide 72: OGC:WCS
GetCapabilities
Same idea as OGC:WMS GetCapabilities
Parameters
  VERSION
  SERVICE
  REQUEST
http://127.0.0.1/cgi-bin/mapserv.exe?map=/ms4w/apps/ms_ogc_workshop/service/config.map&version=1.0.0&service=WCS&request=GetCapabilities

## Slide 73: OGC:WCS
DescribeCoverage
Provides an outline of the structure of a coverage
  bands
  resolution
Parameters
    VERSION
    SERVICE
    REQUEST
    COVERAGE
http://127.0.0.1/cgi-bin/mapserv.exe?map=/ms4w/apps/ms_ogc_workshop/service/config.map&version=1.0.0&service=WCS&request=DescribeCoverage&coverage=toronto

## Slide 74: OGC:WCS
GetCoverage
Gimme data!
Parameters
  VERSION
  SERVICE
  REQUEST
  COVERAGE
  CRS
  BBOX
  E.g.: see index.html

## Slide 75: OGC:WCS
Enabling in MapServer
  MapServer must be built with --with-wcs
  Through metadata elements in mapfile
    “ows_*” or “wcs_*” type metadata
      These drive interface content
    Layers must contain “DUMP TRUE”
    see wcs-server howto

## Slide 76: OGC:SOS
Provides Observations and Measurements
  Sensors
  In-situ
  Monitoring
  e.g. water quality / quantity, weather, air quality
Can Support / Enable:
  Data extraction
  Graphing and trend analysis

## Slide 77: OGC:SOS
Operations
  GetCapabilities
  DescribeSensor
  GetObservation

## Slide 78: OGC:SOS
GetCapabilities
Same idea as OGC:WMS GetCapabilities
Parameters
  VERSION
  SERVICE
  REQUEST
http://127.0.0.1/cgi-bin/mapserv.exe?map=/ms4w/apps/ms_ogc_workshop/service/config.map&version=1.0.0&service=SOS&request=GetCapabilities

## Slide 79: OGC:SOS
DescribeSensor
Provides an outline of the structure of a coverage
  bands
  resolution
Parameters
    VERSION
    SERVICE
    REQUEST
    SENSORID
http://127.0.0.1/cgi-bin/mapserv.exe?map=/ms4w/apps/ms_ogc_workshop/service/config.map&version=1.0.0&service=SOS&request=DescribeSensor&procedure=SOMEID

## Slide 80: OGC:SOS
GetObservation
Gimme data!
Parameters
  VERSION
  SERVICE
  REQUEST
  SENSORID
  CRS
  BBOX
  E.g.: see index.html

## Slide 81: OGC:SOS
Enabling in MapServer
  MapServer must be built with --with-sos (and prerequisites [libxml2])‏
  Through metadata elements in mapfile
    “ows_*” or “sos_*” type metadata
      These drive interface content
    Layers must contain “DUMP TRUE”
    see sos-server howto

## Slide 82: OGC:WMC
Web Map Context Documents
Saves Web Mapping Application State
  remote WMS layer pointers
Like “project” files in common desktop GIS
XML-based

## Slide 83: OGC:WMC
Enabling in MapServer
Check out mapcontext howto
  Handled by MapServer CGI code
    ‘hidden’ API param called “request=GetContext”
      turned OFF by default
  PHP Mapscript methods
      saveMapContext
      loadMapContext
E.gs. and mapfile with context parameters defined:
    http://127.0.0.1/ms_ogc_workshop/context/demo.map
    http://127.0.0.1/ms_ogc_workshop/index.html

## Slide 84: OGC:WMC
Enabling in MapServer
Now MapServer CGI can ingest context
CGI param “context=<url>”
Check out mapcontext howto

## Slide 85: Mapscript WxS
Allows for custom scripting of OGC Web Services via mapscript (perl, python, php, etc.)‏
Can add intermediary layer of logic between OGC requests and responses
  access control
  custom metadata
See MapScript WxS howto

## Slide 86: Wxs : PHP example
http://localhost/ms_ogc_workshop/mapscript/php/ows.php?service=WMS&version=1.1.1&Request=GetCapabilities
<?php
dl("php_mapscript.dll");
$request = ms_newowsrequestobj();
$request->loadparams();
/*forcing the version from 1.1.1 to 1.1.0 */
$request->setParameter("VeRsIoN","1.1.0");
ms_ioinstallstdouttobuffer();
$oMap = ms_newMapobj("../../service/exercise_answer.map");
$oMap->owsdispatch($request);
$contenttype = ms_iostripstdoutbuffercontenttype();
$buffer = ms_iogetstdoutbufferstring();
header('Content-type: application/xml');
echo $buffer;
ms_ioresethandlers();
?>

## Slide 87: Consuming Remote Web Services
Distributed
  Data stays at the source
  You’re getting a ‘view’ of user-specified chunk of data
“middleware”
  Connect to Web Services with software (Perl, Java, PHP, etc.)‏
  Consume XML
  Reformat into HTML
  Use JavaScript for interactive navigation
E.g. Connecting to a world gazetteer WFS to ‘zoom to placename’:
    http://127.0.0.1/ms_ogc_workshop/client/webservices/demo_init.html

## Slide 88: Consuming Remote Web Services
Try rolling your own!
  Add calling button in demo.html
  Create middleware
    Copy/paste gazetteer.php to start off
    Choose a web service to connect to
    Format request and input params
    Figure out XML output structure
    Output with HTML
    Adjust JavaScript if needed
Examples of XML Web Services and sample requests at:
  webservices.txt

## Slide 89: Nice-to-Haves
Official OGC Conformance
  Rubber stamping
Legends for Raster layers
OGC:WMC
  Allowing exposure of local data in a context document
OGC:Filter
  Enhanced support for spatial ops
    Can we use GEOS?

## Slide 90: Future Goodies
Next Generation OGC Services:
  OWS Common
  Unified Constructs
    Metadata
    Operations
    Exceptions
  Now adopted (1.0.0, 1.1.0)‏
  Will be implemented in OGC specs
  WCS 1.1, WFS 1.1, WMS 1.3
OGC SensorWeb is coming
  Thoughts on SensorML, O & M, SOS

## Slide 91: Issues
“Where can I find OGC Web Services”
Canada
  http://geodiscover.cgdi.ca/gdp/search?action=searchForm&entryType=webService
USA
  http://edcw2ks15.cr.usgs.gov/fgdc/EDCgateway.html
  http://gcmd.nasa.gov/
More
  http://www.skylab-mobilesystems.com/en/wms_serverlist.html
  http://wms-sites.com/
User-friendliness of discovery of OGC layers/features/services, etc.

## Slide 92: Contributors
Yewondwossen Assefa
  yassefa at dmsolutions.ca
Jean Francois Doyon
  jdoyon at nrcan.gc.ca
Tom Kralidis
  tom.kralidis at ec.gc.ca
Steve Lime
  steve.lime at dnr.state.mn.us
Daniel Morissette
  dmorisette at mapgears.ca
Jeff McKenna
  jmckenna at gatewaygeomatics.com
Bart van den Eijnden
  bartvde at osgis.nl

## Slide 93: Thanks and Good Luck!
http://ms-ogc-workshop.maptools.org/